#### Table 1.  Crowleys Ridge, Arkansas, Data Acquisition Parameters – November 2006

The data stored in the Analysis/Crowleys Ridge 2006 SEG2 Field Files/ section are raw uncorrelated field records.  See the “Crowleys Ridge observers notes all.pdf” file for details on individual files and comments about the recording process.

Acquisition Parameter

Source array:				Single 9990-kg IVI Minivib I (Thumper; P-wave)

For more source details, see: http://nees.utexas.edu/Equipment-Thumper.shtml

Number of sweeps per station:	up to 4

Vibe point interval:			5 m

Geophones:				Single 8 Hz

Geophone group interval:		5 m

Recording geometry:			144 channels, usually off-end, some walk-throughs

Near trace offset:			usually 10 m

Recording filters:			none

Recording system	:		24-channel Geometrics Geodes

Sampling interval:			0.002 s

Sweep length:				14.0 s

Listen time:				12.0 s

Sweep frequencies:			15-120 Hz (linear)

Output Record length:			2.0 s

Data format:				SEG-2