## Slide 1: An introduction to PDCC the Portable Data Collection Center

## Slide 2: PDCC Overview
The purpose of PDCC is to enable seismic network operators to describe and maintain their instrument metadata in the international FDSN defined SEED format.
PDCC represents a continued effort by IRIS to support the seismological community with tools to enable data management, exchange and research.

## Slide 3: System Requirements
PDCC 3.7 is written in Java and requires Java 5 or 6 to run (Java 6 is recommended). You must install a Java virtual machine (JVM) designed for your computer platform in order to run PDCC, see: http://java.oracle.com
Recommended CPU: 2.0+ GHz, Memory: 1+ GB
Recent Windows, Mac OS X, Linux, and Solaris operating systems are supported. Other systems may be compatible.
Testing has been performed on Mac OS 10.5/10.6, Ubuntu Linux 10.04, and Windows XP SP3.

## Slide 4: Downloading & Installing
You can download PDCC 3.7 from the following URL:
http://www.iris.edu/pub/programs/pdcc/pdcc-3.7.zip
Available on USB drives for Workshop participants
Once you have downloaded the zip file, simply move the file to a directory where you want to carry out the installation and unzip it. For Unix/Linux/Mac OSX you can use the following command:
unzip pdcc-3.7.zip
In some operating systems double-clicking will also unzip.

## Slide 5: PDCC: A hands-on demo

## Slide 6: NRL: Nominal Response Library & The NRL Tool

## Slide 7: SEED Metadata
SEED headers are comprehensive with many required fields. Creating proper SEED metadata requires many details, particularly the channel response information.
The Nominal Response Library (NRL) provides a catalog of response information for many common sensors and data recorders.

## Slide 8: The IRIS Nominal Response Library
http://www.iris.edu/NRL
Verified with the manufacturer
Integrated into PDCC using NRL Tool
Flexible design for updates and merging

## Slide 9: NRL Components
Each instrument and digitizer in the NRL is represented by a SEED RESP file.
Categorized by equipment type and manufacturer
HTML web pages for detailed information not readily available elsewhere

## Slide 10: NRL Tool
Features:
Integrated into PDCC
Selection of complete instrument (sensor and data logger) from NRL
Merging NRLs (e.g. IRIS and local)

## Slide 11: How to launch NRL Tool in PDCC

## Slide 12: NRL Tool Demo
Important:
A channel (Blockette 052) must be selected before launching NRL Tool
NRL Tool will replace the response information for the selected channel