## Slide 1: IRIS QA Network Reports - Evaluating Issues
Tools to better understand what the metrics are telling us

## Slide 2
QA Reports – A Brief Outline
Now that we have a list of issues…
Cover some common issues and the thresholds that find them
  Knowing what issues arise from certain thresholds can make the evaluation process quicker
Go over the GUI used to keep track of issues
  This was created as a mechanism to simplify the evaluation process, allowing easy access to tools like PDFs and MUSTANG metrics
Delve into the code so that you can adapt it where necessary
  Adapting the code to your own network and own needs can make it a more useful tool
A quick look at the ticketing system we use at the DMC
  While we use our own ticketing system, you may want to include similar information

## Slide 3
Process:
Find Issues
Evaluate Issues
Generate Report
Process:
Find Issues
Evaluate Issues
Generate Report
Use web services and waveform review to look at issues
QA Reports – Evaluating Issues

## Slide 4
QA Reports – Evaluating Issues
Some issues come up more frequently – dependent on network, environmental difficulties, instrumentation, telemetry setups, etc, etc.
Completeness:
  Gaps and outages
Amplitudes:
  Masses off center, re-centering, or hitting stops
  Shifting vaults and seasonal fluctuations
  Metadata issues
  Instrument damage
  Signal fluctuations and losses
  Power cycles
Common Issues

## Slide 5
QA Reports – Evaluating Issues
Completeness: gaps and outages
Common thresholds:
noData
gapRatioGt012
avgGaps
GOAT and Databrowser are useful for finding patterns in outages and gaps
Sensor vs transmission: spatial patterns, signals in the data
http://ds.iris.edu/data_available/IU/ANMO/*/BH*?scaling=time_range&byday=off&timewindow=2018/01/01-2018/07/01
Common Issues

## Slide 6
QA Reports – Evaluating Issues
Masses off center or hitting stops
Common thresholds:
xTalk
nSpikes
noise1
noise2
dcOffsets
hiAmp
Common Issues

## Slide 7
QA Reports – Evaluating Issues
Dead channels
Common thresholds:
lowAmp
lowRms
Dead
Flat
Common Issues

## Slide 8
QA Reports – Evaluating Issues
Diurnal signals and seasonal fluctuations
Common thresholds:
xTalk
rmsRatio
dcOffsets
Common Issues

## Slide 9
QA Reports – Evaluating Issues
Signal Fluctuations
Common thresholds:
lowAmp
lowRms
Common Issues

## Slide 10
QA Reports – Evaluating Issues
Common Issues
Signal Fluctuations
Common thresholds:
hiAmp
lowAmp

## Slide 11
doQA
Examining Issues
GUI to facilitate manual look at flagged issues
Python code
Preference file optional
Examine Issues
Issues File
Preference
File
Issues File
(altered)
OR: python QuARG.py /path/to/report.txt
QA Reports – Evaluating Issues

## Slide 12
QuARG as a utility
The MUSTANG thresholds have indicated an issue, now what?
Different issues have different tools that are more readily useful
Data availability
  Web Services
  Databrowser
  GOAT
Amplitudes
  PDFs
  Waveform review
  Databrowser
The most common tools I use are included in the GUI, but it’s not an exhaustive list
QA Reports – Evaluating Issues
QuARG

## Slide 13
Examine Issues
Issues File
Preference
File
Issues File
(altered)
./QuARG.py /Users/laura/QA_REPORTS/AK_reports/AK/201805/report.orig
QuARG.py
Issues Pane
List of issues
Status
Threhold
Target
N.S.
Start date
End date
N days
Notes
Check boxes to select particular lines
QA Reports – Evaluating Issues
QuARG

## Slide 14
Examine Issues
Issues File
Preference
File
Issues File
(altered)
./QuARG.py /Users/laura/QA_REPORTS/AK_reports/AK/201805/report.orig
QuARG.py
Input Pane
Metric – used to look up MUSTANG metrics. Default: percent_availability
Start Date – beginning of timespan. Default: first day of last month
End Date – end of timespan. Default: first day of this month
SNCL – target, including wildcards. Defaults to NET.STA.*.*H*
Notes – field to add notes
QA Reports – Evaluating Issues
QuARG

## Slide 15
Examine Issues
Issues File
Preference
File
Issues File
(altered)
./QuARG.py /Users/laura/QA_REPORTS/AK_reports/AK/201805/report.orig
QuARG.py
Tool Pane
Create Ticket – opens a web page to our ticketing system
Databrowser – opens a web page with databrowser
See Metrics – web page with the listed metrics for the SNCL and dates specified
See PDFs – web page of the PDF browser for SNCL specified
GOAT – web page with GOAT availability for SNCL and dates specified
Events – web page to the USGS event service for dates specified, >5.5M
Station – web page to IRIS station service for station specified
Next – next station
Previous – previous station
Todo – toggle; see only TODO issues, grouped by station like normal
Remaining – toggle; see all TODO issues in one list
Exit – exit (make sure to save first)
QA Reports – Evaluating Issues
QuARG

## Slide 16
Examine Issues
Issues File
Preference
File
Issues File
(altered)
./QuARG.py /Users/laura/QA_REPORTS/AK_reports/AK/201805/report.orig
QuARG.py
Status Pane
Mark status as Open
Mark status as Closed
Mark status as pre-existing ticket
Mark status as support ticket
Mark status as Not Ticketing
Mark status as False Positive
Add Notes to selected lines
Save work (to report.txt)
QA Reports – Evaluating Issues
QuARG

## Slide 17
Dependencies:
  sys, os, pandas, numpy, Tkinter, webbrowser, datetime
Examine Issues
Issues File
Preference
File
Issues File
(altered)
QuARG.py
Goal: understand the structure enough to make changes if necessary to adapt to your network and your reports.
The ExamineIssues class is where the GUI is created. Within there, there are these main sections:
  Set up the “Frames” for each section
  Create buttons and input fields, place them in the layout
  Define tasks for the buttons
QA Reports – Evaluating Issues
QuARG

## Slide 18
QA Reports – Evaluating Issues
The ticketing system we use
Powered by Redmine
Project for each network
Custom queries
Easy to track
Fields for:
Start and end
Status
Metrics used
Descriptions
Images